## Slide 1: CABLES Prepared By: pranav chaudhari parul institute of engineering, waghodiya

## Slide 2
A cable is most often two or more wires running side by side and bonded, twisted, or braided together to form a single assembly, but can also refer to a heavy strong rope.

## Slide 3: MAIN CABLE COMPONENTS
An electric cable is made up of a conductor, which channels the electricity flow, and an insulation that contains this electricity flow in the conductor. Moreover, other auxiliary elements can be included which ensure its longevity.
The conductor is where the electric current is actually transmitted, with copper being generally the most used material.
The insulation is the layer of polymer, plastic or elastomer which surrounds the conductor and insulates it from external contact.

## Slide 4: TYPES OF CABLES
Fiber-Optic Cable: Optical fiber is usually used for longer, high bandwidth, point-to-point transmission. The fiber-optic cable uses light to transmit data through thin glass or plastic fiber. Electrical signals cause a fiber-optic transmitter to generate the light signals sent down the fiber. The receiving host receives the light signals and converts them to electrical signals. The glass used in fiber-optic cable acts as an electrical insulator. No electricity is used in the fiber-optic cable.

## Slide 5: TYPES OF CABLES
Coaxial Cable: Coaxial cable is made up of a copper conductor surrounded by a layer of flexible insulation. The center conductor can also be made of tin plated aluminum cable allowing for the cable to be manufactured inexpensively. Over this insulating material is a woven copper braid or metallic foil that acts as the second wire in the circuit and as a shield for the inner conductor. This second layer, or shield also reduces the amount of outside electromagnetic interference. Covering this shield is the cable jacket. Cable television uses coaxial cable.

## Slide 6: TYPES OF CABLES
Shielded Twisted Pair : STP cable uses cancellation, shielding, and twisted wires. The twisted wires and shielded twisted-pair cables allow for more cancellation of electrical interference than the unshielded twisted-pair cables. Each pair of wires is wrapped in metallic foil and those four pairs of wires are wrapped in an overall metallic foil.

## Slide 7: TYPES OF CABLES
Unshielded Twisted Pair : UTP is a four-pair wire medium used in a variety of networks. Each of the eight copper wires in the UTP cable is covered by insulating material. In addition, each pair of wires is twisted around each other. This type of cable relies on the cancellation effect produced by the twisted wire pairs to limit attenuation3 caused by electromagnetic interference and radio frequency interference.

## Slide 8: COLOR CODE
To enable wires to be easily and safely identified, all common wiring safety codes mandate a colour scheme for the insulation on power conductors. In a typical electrical code, some colour-coding is mandatory, while some may be optional. Many local rules and exceptions exist. Older installations vary in colour codes, and colours may shift with insulation exposure to heat, light, and aging.
Many electrical codes now recognize (or even require) the use of wire covered with green insulation, additionally marked with a prominent yellow stripe, for safety grounding (earthing) connections. This growing international standard was adopted for its distinctive appearance, to reduce the likelihood of dangerous confusion of safety grounding wires with other electrical functions, especially by persons affected by red-green colour blindness.

## Slide 9: PROPERTIES
Electric Properties:
- dielectric strength
- insulation resistance
- insulation power factors
- charging current
- arc resistance
tracking susceptibility
Mechanical Properties:
- toughness and flexibility
- tensile, elongation and crushing strengths
- resistance to abrasion or moisture
Brittleness
Chemical Properties:
- moisture absorption
- resistance to oil, gas, acids and alkalis
stability when exposed to sunlight, ozone, or flames
Thermal Properties:
- expansion and contraction
- softening and flow temperature
- compatibility with operating, ambient, or emergency overload and short circuit conditions

## Slide 10: CONDUCTOR MATERIALS
Copper
The principal electrical conductor due to its excellent conductivity and reasonable cost.
Aluminum
61% the conductivity and .3027 times the weight of copper. Used in power cables, overhead (ACSR), and some building wire.
Copper weld
A thin coating of copper fused to a steel core. Used in line wire, cable messengers and stranded with copper for strength or extending flex life.
Alum weld
A thin coating of aluminum fused to a steel core. Used in line wire and cable messengers.
Tinsel
Flat ribbons of bronze, silver, or copper alloy spiraled around a textile core of cotton, nylon, etc. Used in telephone and electronics applications as conductors in line cords, microphone cords, and retractile cords.
Thermocouple
Special matched Alloy Conductors. Used in temperature measuring applications

## Slide 11: References
en.wikipedia.org/wiki/Cable‎
https://en.wikipedia.org/wiki/Electrical_wiring‎
Elements of Electrical Engineering By U.A.Patel

## Slide 12: THE END